## Slide 1: Design and Simulation of TPS Worldwide’s Network Infrastructure (Blueprint-Based Implementation in Cisco Packet Tracer)
Syeda Maham Ikram (23SP-101-CS)
Fizza Mubben (23SP-070-CS)
Mahnoor Nadeem (23SP-065-CS)
Rabbania Akhter (23SP-064-CS)

## Slide 2: Project overview
Designed a simulated enterprise-grade network
Based on a blueprint requested from TPS Worldwide (Karachi-based fintech firm)
Implemented using Cisco Packet Tracer
Key Goals :
Logical Segmentation:
Each department (e.g., Dev – VLAN 10, HR – VLAN 30) is isolated using VLANs to reduce broadcast traffic.
Centralized Services:
DHCP, DNS, FTP, and Web servers hosted in Server VLAN 50, accessible to all departments.
Secure Inter-VLAN Communication:
Controlled via a Layer 3 core switch, allowing only necessary cross-department access.
Scalable & Testable:
Network supports 180+ devices; new departments can be added via VLANs; services tested end-to-end.

## Slide 3: Objectives
Simulate a multi-department enterprise network
Use VLANs for logical traffic separation between departments
Design a two-tier topology with Core and Access layers
Configure essential network services:
  DHCP – for automatic IP assignment
  DNS – for internal domain name resolution
  FTP – for file sharing across departments
  Web Server – for intranet access (HTTP)
Validate end-to-end connectivity, service availability, and inter-VLAN routing
Build a simple yet effective network that also helps practice key exam topics like VLANs, inter-VLAN routing, DHCP, DNS, and FTP configuration

## Slide 4: Network Architecture
Core Layer:
  Cisco Catalyst 3560 (Layer 3)
  Handles inter-VLAN routing via SVIs
  Directly connected to all access switches and servers
Access Layer:
  One Layer 2 switch per department
  Connects PCs, printers, and wireless devices
Internet Simulation:
  Via Cisco 2911 routers
  Internet router connected to core router

## Slide 5: VLAN and IP Design
Department | VLAN | Subnet | Gateway IP
Development | 10 | 192.168.10.0/24 | 192.168.10.1
QA | 20 | 192.168.20.0/24 | 192.168.20.1
HR | 30 | 192.168.30.0/24 | 192.168.30.1
Admin/Finance | 40 | 192.168.40.0/24 | 192.168.40.1
Servers | 50 | 192.168.50.0/24 | 192.168.50.1
Management | 60 | 192.168.60.0/24 | 192.168.60.1
Guest Wi-Fi | 70 | 192.168.70.0/24 | 192.168.70.1

## Slide 6: Server Infrastructure
All services hosted in VLAN 50
Static IPs for servers:
DHCP Server – 192.168.50.10
DNS Server – 192.168.50.20
FTP Server – 192.168.50.30
Web Server – 192.168.50.40
Centralized and directly connected to Core Switch
Accessible across all departments

## Slide 7: Key Configurations
VLANs created and assigned to access switch ports for each department
Trunk links established between access switches and the core Layer 3 switch
SVIs (Switched Virtual Interfaces) configured on the core switch for inter-VLAN routing
DHCP Pools set up per VLAN for dynamic IP allocation
DNS A-records created for internal services (e.g., ftp.tps.com, intranet.tps.com)
FTP and Web servers tested successfully with login and browser access
Internet Router connected to Guest VLAN (VLAN 70) → Guest laptop verified internet access through this router

## Slide 8: Testing & Validation
✅ Intra-VLAN Communication
✅ Inter-VLAN Routing via Core Switch
✅ DHCP lease assignment to clients
✅ DNS hostname resolution
✅ FTP file transfers (Dev & QA)
✅ Internal web server access via browser
✅ Internet connectivity (simulated router)

## Slide 9: Conclusion
Successfully built a simulated enterprise network based on the blueprint provided by TPS Worldwide
Demonstrated key enterprise networking concepts including:
VLAN segmentation
Inter-VLAN routing via SVIs
Centralized server services (DHCP, DNS, FTP, Web)
Simulated internet access
Conducted thorough testing and validation to ensure full end-to-end connectivity
The design reflects real-world scalability, security, and industry best practices
Also serves as a comprehensive practice project for key exam topics and hands-on learning